Infrared Presence Detector – Presence Control PRO IR Quattro SLIM XS-R COM1

- For offices, conference rooms, classrooms and side rooms

- Super flat 360° infrared presence detector

- 16 m² square presence detection area

- Only 6 mm visible after ceiling installation

- Fits in every mounting box

- Unique retina lens

- Optional: User remote control RC5, service remote control RC8, Smart Remote

Technical specifications:

Voltage:				220-240V, 50/60Hz

Output:	max. 1000 W (ohmic  loads)

max. 8 LEDs/Energysaving lamps,  C<176µF (capacitive)

Detection range:			4m x 4 m  presence, radial, tangential

Detection angle: 			360°

Response brightness:  	10-1000 Lux

Time setting:	30 Sec. – 30 Min., IQ

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP-/Protection class:		IP 20

Marks of conformity:		CE, DEKRA

Operating temperature:		0°C - +40°C

Abmessungen (H x B x T):		Ø94 x 55 mm

Colour:				white

Warranty:				5 Jahre

Article number:			035211

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de